## Slide 1: Fundamentals of Seismic Refraction Theory, Acquisition, and Interpretation
Craig Lippus
Manager, Seismic Products
Geometrics, Inc.
December 3, 2007

## Slide 2: Geometrics, Inc.
Owned by Oyo Corporation, Japan
In business since 1969
Seismographs, magnetometers, EM systems
Land, airborne, and marine
80 employees

## Slide 3: Located in San Jose, California

## Slide 4: Fundamentals of Seismic Waves
What is a seismic wave?

## Slide 5: Fundamentals of Seismic Waves
Transfer of energy by way of
particle motion.
Different types of seismic waves are characterized by their particle motion.
What is a seismic wave?

## Slide 6: Three different types of seismic waves
Compressional (“p”) wave
Shear (“s”) wave
Surface (Love and Raleigh) wave
Only p and s waves (collectively referred to
as “body waves”) are of interest
in seismic refraction.

## Slide 7: Compressional (“p”) Wave
Identical to sound wave – particle
motion is parallel to propagation
direction.
Animation courtesy Larry Braile, Purdue University

## Slide 8: Shear (“s”) Wave
Particle motion is perpendicular
to propagation direction.
Animation courtesy Larry Braile, Purdue University

## Slide 9: Velocity of Seismic Waves
Depends on density elastic moduli
where K = bulk modulus,  = shear modulus, and  = density.

## Slide 10: Velocity of Seismic Waves
Bulk modulus = resistance to compression = incompressibility
Shear modulus = resistance to shear = rigidity
The less compressible a material is, the greater its p-wave velocity, i.e., sound travels about four times faster in water than in air. The more resistant a material is to shear, the greater its shear wave velocity.

## Slide 11
Q. What is the rigidity of water?

## Slide 12: A. Water has no rigidity. Its shear strength is zero.
Q. What is the rigidity of water?

## Slide 13: Q. How well does water carry shear waves?

## Slide 14: A. It doesn’t.
Q. How well does water carry shear waves?

## Slide 15
Fluids do not carry shear waves. This knowledge, combined with earthquake observations, is what lead to the discovery that the earth’s outer core is a liquid rather than a solid – “shear wave shadow”.

## Slide 16: p-wave velocity vs. s-wave velocity
p-wave velocity must always be greater than s-wave velocity. Why?
K and  are always positive numbers, so Vp is always greater than Vs.

## Slide 17: Velocity – density paradox
Q. We know that in practice, velocity tends to be directly proportional to density. Yet density is in the denominator. How is that possible?

## Slide 18: Velocity – density paradox
A. Elastic moduli tend to increase with density also, and at a faster rate.
Q. We know that in practice, velocity tends to be directly proportional to density. Yet density is in the denominator. How is that possible?

## Slide 19: Velocity – density paradox
Note: Elastic moduli are important parameters for understanding rock properties and how they will behave under various conditions. They help engineers assess suitability for founding dams, bridges, and other critical structures such as hospitals and schools.
Measuring p- and s-wave velocities can help determine these properties indirectly and non-destructively.

## Slide 20: Q. How do we use seismic waves to understand the subsurface?

## Slide 21: Q. How do we use seismic waves to understand the subsurface?
Must first understand wave
behavior in layered media.

## Slide 22: Q. What happens when a seismic wave encounters a velocity discontinuity?

## Slide 23: Q. What happens when a seismic wave encounters a velocity discontinuity?
A. Some of the energy is reflected, some is refracted.
We are only interested in refracted energy!!

## Slide 24: Q. What happens when a seismic wave encounters a velocity discontinuity?

## Slide 25
Five important concepts
Seismic Wavefront
Ray
Huygen’s Principle
Snell’s Law
Reciprocity

## Slide 26
Q. What is a seismic wavefront?

## Slide 27: Q. What is a seismic wavefront?
A. Surface of constant phase, like ripples on a pond, but in three dimensions.

## Slide 28: Q. What is a seismic wavefront?

## Slide 29
The speed at which a wavefront travels is the seismic velocity of the material, and depends on the material’s elastic properties. In a homogenious medium, a wavefront is spherical, and its shape is distorted by changes in the seismic velocity.

## Slide 30: Seismic wavefront

## Slide 31: Q. What is a ray?

## Slide 32: Q. What is a ray?
A. Also referred to as a “wavefront
normal” a ray is an arrow
perpendicular to the wave front,
indicating the direction of travel at
that point on the wavefront. There
are an infinite number of rays on a
wave front.

## Slide 33: Ray

## Slide 34: Huygens' Principle
Every point on a wave front can be thought of as a new point source for waves generated in the direction the wave is traveling or being propagated.

## Slide 35
Q. What causes refraction?

## Slide 36: Q. What causes refraction?
A. Different portions of the wave front reach the velocity boundary earlier than other portions, speeding up or slowing down on contact, causing distortion of wave front.

## Slide 39: Understanding and Quantifying How Waves Refract is Essential

## Slide 40
Snell’s Law
(1)

## Slide 41
Snell’s Law
If V2>V1, then as i increases, r increases faster

## Slide 42
Snell’s Law
r approaches 90o as i increases

## Slide 43
Snell’s Law
Critical Refraction
At Critical Angle of incidence ic, angle of refraction r = 90o
(2)
(3)

## Slide 44
Snell’s Law
Critical Refraction
At Critical Angle of incidence ic, angle of refraction r = 90o

## Slide 45
Snell’s Law
Critical Refraction
At Critical Angle of incidence ic, angle of refraction r = 90o

## Slide 46
Snell’s Law
Critical Refraction
Seismic refraction makes use of critically refracted, first-arrival energy only. The rest of the wave form is ignored.

## Slide 47: Principal of Reciprocity
The travel time of seismic energy between two points is independent of the direction traveled, i.e., interchanging the source and the geophone will not affect the seismic travel time between the two.

## Slide 48: Using Seismic Refraction to Map the Subsurface
Critical Refraction Plays a Key Role

## Slide 50
(Snell’s Law)

## Slide 51
From Snell’s Law,
(4)

## Slide 52: Using Seismic Refraction to Map the Subsurface

## Slide 53: Using Seismic Refraction to Map the Subsurface

## Slide 54: Using Seismic Refraction to Map the Subsurface

## Slide 55: Using Seismic Refraction to Map the Subsurface

## Slide 56: Using Seismic Refraction to Map the Subsurface

## Slide 57: Using Seismic Refraction to Map the Subsurface

## Slide 58: Using Seismic Refraction to Map the Subsurface

## Slide 59: Using Seismic Refraction to Map the Subsurface

## Slide 60: Using Seismic Refraction to Map the Subsurface

## Slide 61: Using Seismic Refraction to Map the Subsurface

## Slide 62: Using Seismic Refraction to Map the Subsurface

## Slide 63: Using Seismic Refraction to Map the Subsurface

## Slide 64: Using Seismic Refraction to Map the Subsurface

## Slide 65: Using Seismic Refraction to Map the Subsurface

## Slide 66: Using Seismic Refraction to Map the Subsurface

## Slide 67: Using Seismic Refraction to Map the Subsurface

## Slide 68: Using Seismic Refraction to Map the Subsurface

## Slide 69: Using Seismic Refraction to Map the Subsurface

## Slide 70: Using Seismic Refraction to Map the Subsurface

## Slide 71: Using Seismic Refraction to Map the Subsurface
Depth{
(5)

## Slide 72: Using Seismic Refraction to Map the Subsurface
Depth{
For layer parallel to
surface
(6)

## Slide 73
Summary of Important Equations
For refractor parallel to surface
(2)
(3)
(1)
(5)
(4)
(6)
Snell’s Law

## Slide 79: Crossover Distance vs. Depth

## Slide 80: Depth/Xc vs. Velocity Contrast

## Slide 81: Important Rule of Thumb
The Length of the Geophone Spread Should be 4-5 times the depth of interest.

## Slide 82: Dipping Layer
Defined as Velocity Boundary
that is not Parallel to Ground Surface
You should always do a minimum of one shot at either end the spread. A single shot at one end does not tell you anything about dip, and if the layer(s) is dipping, your depth and velocity calculated from a single shot will be wrong.

## Slide 83: Dipping Layer
If layer is dipping (relative to ground surface), opposing travel time curves will be asymmetrical.
Updip shot – apparent velocity > true velocity
Downdip shot – apparent velocity < true velocity

## Slide 84: Dipping Layer

## Slide 85
Dipping Layer

## Slide 86
Dipping Layer
From Snell’s Law,

## Slide 87
Dipping Layer
The true velocity V2 can also be calculated by multiplying the harmonic mean of the up-dip and down-dip velocities by the cosine of the dip.

## Slide 88
What if V2 < V1?

## Slide 89
What if V2 < V1?
Snell’s Law

## Slide 90
What if V2 < V1?
Snell’s Law

## Slide 91
If V1>V2, then as i increases, r increases, but not as fast.
What if V2 < V1?

## Slide 92
If V2<V1, the energy refracts toward the normal.
None of the refracted energy makes it back to the surface.
This is called a velocity inversion.

## Slide 93
Seismic Refraction requires that velocities increase with depth.
A slower layer beneath a faster layer will not be detected by seismic refraction.
The presence of a velocity inversion can lead to errors in depth calculations.

## Slide 101: Delay Time Method
Allows Calculation of Depth Beneath Each Geophone
Requires refracted arrival at each geophone from opposite directions
Requires offset shots
Data redundancy is important

## Slide 102: Delay Time Method
x
V1
V2

## Slide 103: Delay Time Method
x
V1
V2

## Slide 104: Delay Time Method
x
V1
V2

## Slide 105: Delay Time Method
x
V1
V2

## Slide 106: Delay Time Method
x
Definition:
V1
V2
(7)

## Slide 108
But from figure above,
. Substituting, we get
or

## Slide 109
Substituting from Snell’s Law,

## Slide 110
Multiplying top and bottom by sin(ic)

## Slide 111
Substituting from Snell’s Law,
(8)
We get

## Slide 112
(9)

## Slide 113
Reduced Traveltimes
Definition:
T’AP = “Reduced Traveltime” at point P for a source at A
T’AP=TAP’
x
Reduced traveltimes are useful for determining V2. A plot of T’ vs. x will be roughly linear, mostly unaffected by changes in layer thickness, and the slope will be 1/V2.

## Slide 114
Reduced Traveltimes
x
From the above figure, T’AP is also equal to TAP minus the Delay Time. From equation 9, we then get

## Slide 115
Reduced Traveltimes
x
Earlier, we defined to as
Substituting, we get
(7)
(10)

## Slide 116
Reduced Traveltimes
Finally, rearranging yields
The above equation allows a graphical determination of the T’ curve. TAB is called the reciprocal time.
(11)

## Slide 117
Reduced Traveltimes
The first term is represented by the dotted line below:

## Slide 118
Reduced Traveltimes
The numerator of the second term is just the difference in the traveltimes from points A to P and B to P.

## Slide 119
Reduced Traveltimes
Important: The second term only applies to refracted arrivals. It does not apply outside the zone of “overlap”, shown in yellow below.

## Slide 120
Reduced Traveltimes
The T’ (reduced traveltime) curve can now be determined graphically by adding (TAP-TBP)/2 (second term from equation 9) to the TAB/2 line (first term from equation 9). The slope of the T’ curve is 1/V2.

## Slide 121
We can now calculate the delay time at point P. From Equation 10, we see that
According to equation 8
So
Now, referring back to equation 4
(12)
(4)
(8)
(10)

## Slide 122
It’s fair to say that
Combining equations 12 and 13, we get
Or
(13)
(14)

## Slide 123
Referring back to equation 9, we see that
Substituting into equation 14, we get
Or
Solving equation 9 for hp, we get
(15)
(16)
(9)

## Slide 124
We know that the incident angle i is critical when r is 90o. From Snell’s Law,

## Slide 125
Substituting back into equation 16,
(16)
(17)
we get

## Slide 126
In summary, to determine the depth to the refractor h at any given point p:

## Slide 127
1.Measure V1 directly from the traveltime plot.

## Slide 128
2.Measure the difference in traveltime to point P from opposing shots (in zone of overlap only).

## Slide 129
3.Measure the reciprocal time TAB.

## Slide 130
4. Per equation 11,
divide the reciprocal time TAB by 2.
,

## Slide 131
5. Per equation 11,
add ½ the difference time at each point P to TAB/2 to get the reduced traveltime at P, T’AP.
,

## Slide 132
6. Fit a line to the reduced traveltimes, compute V2 from slope.

## Slide 133
7. Using equation 15,
Calculate the Delay Time DT at P1, P2, P3….PN
(15)

## Slide 134
8. Using equation 17,
Calculate the Depth h at P1, P2, P3….PN
(16)

## Slide 135: That’s all there is to it!

## Slide 147
More Data is Better Than Less

## Slide 148
More Data is Better Than Less

## Slide 149
More Data is Better Than Less

## Slide 150
More Data is Better Than Less

## Slide 151
More Data is Better Than Less

## Slide 152
More Data is Better Than Less

## Slide 153
More Data is Better Than Less

## Slide 154
More Data is Better Than Less

## Slide 155
More Data is Better Than Less

## Slide 156
More Data is Better Than Less